## Slide 1: Introduction to the Vertex Skeleton “Vskel” Library
Methods to shrink 2D and higher polytopes, and to approximate medial axes
Photo by <a href="https://unsplash.com/@fakurian?utm_content=creditCopyText&utm_medium=referral&utm_source=unsplash">Milad Fakurian</a> on <a href="https://unsplash.com/photos/a-black-and-white-photo-of-a-diamond-0uUzrqDeBNY?utm_content=creditCopyText&utm_medium=referral&utm_source=unsplash">Unsplash</a>

## Slide 2: For many examples below, MATLAB code will be given. It is usually highlighted as shown here: yellow for scripts, grey for console outputs.
%% Example 1: simple three points
fig_num = 1;
x = [-4; -2; 1];
y = [0; -4; -1];
apex_points = [x y];
fcn_FastestTraversal_calculateObstacleDirectionAtApexPoints(...
apex_points, fig_num);
>> script_test_fcn_geometry_selfCrossProduct
cross_products =
0
err =
1

## Slide 3: Each function uses a class-specific argument check function
function fcn_MapGen_checkInputsToFunctions(...
variable,variable_type_string,varargin)
% fcn_MapGen_checkInputsToFunctions
% Checks the variable types commonly used in the MapGen codes to
% ensure they are correctly formed.
%
% This function is typically called at the top of most functions. The input
% is a variable and a string defining the "type" of the variable. This
% function checks to see that they are compatible. For example, say there
% 'column_vector' type of variables used in the function that is always a N
% x 1 array; if someone had a variable called "test_example", they could
% check that this fit the 'column_vector' type by calling
% fcn_MapGen_checkInputsToFunctions(test_example,'column_vector').
% This function would then check that the array was N x 1, and if it was
% not, it would send out an error warning.
%
% FORMAT:
%
% fcn_MapGen_checkInputsToFunctions(...
% variable,variable_type_string,(optional_arguments))
%
% INPUTS:
%
% variable: the variable to check
See: script_test_fcn_MapGen_checkInputsToFunctions.m for example usages

## Slide 4: A demonstration script exists that shows most of the functionality in this document: script_demo_MapGenLibrary
%% Show how inputs are checked
Twocolumn_of_numbers_test = [4 1; 3 0; 2 5];
fcn_MapGen_checkInputsToFunctions(Twocolumn_of_numbers_test, '2column_of_numbers');
%% Generate a set of polytopes from various pseudo-random sources
% Generate a set of polytopes from the Sobol set
fig_num = 11;
Sobol_range = [1 1000]; % range of Sobol points to use to generate the tiling
tiled_polytopes = fcn_MapGen_sobolVoronoiTiling(Sobol_range,[1 1],fig_num);
% Generate a set of polytopes from the Halton set
fig_num = 12;
Halton_range = [1 1000]; % range of Halton points to use to generate the tiling
tiled_polytopes = fcn_MapGen_haltonVoronoiTiling(Halton_range,[1 1],fig_num);

## Slide 5: Shrink from Edges Functionality
Updated 2025-04-29 by S. Brennan

## Slide 6: Individual polytopes can be shrunk by edges, and the first step is to find the Vertex Skeleton via: fcn_MapGen_polytopeFindVertexSkeleton This function defines how the vertices “move” as edges are trimmed inward by the same amount.
fig_num = 675;
vertices = [0 0; 2 0; 1 2; 0 1; 0 0]*5;
fcn_MapGen_polytopeFindVertexSkeleton(vertices,fig_num);

## Slide 7: The skeleton is calculated by iterating inward from the given vertices
As long as there are more than 2 vertices, it:
Calculates the vectors pointing inward, and angles they make relative to next segment (“half angles”)
Using the angles and vectors, calculates where the vectors intersect
Finds the minimum distance of intersection
Merges vertices that come together
Repeats

## Slide 8: Step 1: To calculate the vectors inward, the function calls an internal function to obtain unit vectors inward, the half angles, the distances from vertex-to-vertex, and unit vectors from vertex to vertex.
[vector_direction_of_unit_cut, ...
half_angles,...
distances_vertex_to_vertex,...
unit_vectors_vertex_to_vertex] = ...
INTERNAL_fcn_findUnitDirectionVectors(working_vertices,333);

## Slide 9: To calculate the intersection points, the following geometry is used to find , and the projection point where the edge projects inward directly toward the intersection.
D

## Slide 10: Using the half-angles to define the theta1 and theta2 values, one can find the projection points from each edge
These projection points are where the orthogonal from each edge would intersect the vertices, as vertices shrink inward and touch each other.

## Slide 11: We next rotate the unit vectors from one corner to another by 90 degrees, and starting from the projection points, move inward by Lcut. This predicts the intersection points of the vertices.

## Slide 12: The minimum cut distance defines how far we can cut inward before vertices merge. The indices that merge have to have the same cut distance and follow one after the other.
Once we know which vertex is the closest, we need to move all vertices inward by ONLY the shortest cut distance.

## Slide 13: Before starting on the next step, in case there are only 2 points left, we calculate the vector direction of the unit cuts for the new vertices just created.
These are just the average of the adjacent vectors that were merged. This is repeated until all the points converge, or only 2 points are left

## Slide 14: The final result is the skeleton plot
The outputs give:
new_vertices: a cell array of dimension M, where each index 1:M stores a N x 2 array of the coordinates of the nested shape inside, with M = 1 being the starting shape (and with dimension K+1, where K is number of vertices given), and N being smaller and smaller for each M value.
new_projection_vectors: a cell array of M, where each index 1:M stores a L x 2 array of the unit vectors (with L = N-1) that point away from the vertices of the nested shape inside, with M = 1 being the starting unit vectors (and with dimension K, where K is number of vertices given), and L being smaller and smaller for each M value.
cut_distance: a cell array of M, ranging from 0 (for M=1) to the maximum cut distance that can be used

## Slide 15: To use this, we index the template corresponding to our cut depth, and cut more if needed
fig_num = 675;
vertices = [0 0; 2 0; 1 2; 0 1; 0 0]*5;
[new_vertices, new_projection_vectors, cut_distance] = fcn_MapGen_polytopeFindVertexSkeleton(vertices,fig_num);
figure(4747);
grid on
grid minor
hold on
axis equal
for cut = 0:0.5:cut_distance(end)
% Find the shape that is less than or equal to the cut
shape_index = find(cut_distance<=cut,1,'last');
% Grab vertices to start from, cut to start from
starting_vertices = new_vertices{shape_index};
starting_cut = cut_distance(shape_index);
% Calculate projection distance
projection_distance = cut - starting_cut;
% Determine final vertices
final_vertices = starting_vertices + new_projection_vectors{shape_index}*projection_distance;
% Plot results
plot(final_vertices(:,1),final_vertices(:,2),'r.-','Linewidth',2,'Markersize',20);
end

## Slide 16: Here’s other examples:
Square:
Wide Rectangle:
Tall Rectangle:
Goofy Polytope:
See: script_test_fcn_MapGen_polytopeFindVertexSkeleton
For more examples
Random Polytope:

## Slide 17: The function fcn_MapGen_polytopeShrinkFromEdges implements the skeleton calculations to perform the shrinkage
This is implemented in three steps:
1. Calculate the polytope skeleton, or use the skeleton if the user
provides this as inputs.
2. Using the cut distance, find the template that is less than or equal
to the cut distance. If less, then calculate the additional cut and
project the verticies to their new points based on residual cut.
3. Convert the resulting verticies into the standard polytope form.

## Slide 18: The code that performs the cutting is relatively simple. It uses the largest template that corresponds to a cut smaller or equal to the requested cut.
%% STEP 2. Using the cut distance, find the template
% We want to use the one that is less than or equal to the cut distance. If
% less, then calculate the additional cut and project the verticies to
% their new points based on residual cut.
% Find the shape that is less than or equal to the cut
shape_index = find(cut_distance<=edge_cut,1,'last');
% Grab vertices to start from, cut to start from
template_vertices = new_vertices{shape_index};
template_start_cut = cut_distance(shape_index);
% Calculate projection distance
additional_cut_distance = edge_cut - template_start_cut;
% Determine final vertices
final_vertices = template_vertices + new_projection_vectors{shape_index}*additional_cut_distance;

## Slide 19: The results are as expected
Square:
Right Triangle:
Right Triangle Cut too Deeply
Repeated cuts:
See: script_test_fcn_MapGen_polytopeFindVertexSkeleton
For more examples

## Slide 20: When using edge cutting, particularly if repeatedly using this, significant computation time is saved if one avoids repeated calculation of the skeleton.
If one precomputes, this and reuses it, it can save roughly 10 times the computation. If one avoids polytope calculations and just needs the vertices, it saves roughly 100 times the calculations

## Slide 21: How to Shrink from Edges with Non-Convex Polytopes
Updated 2025-04-19 by S. Brennan

## Slide 22: For non-convex polytopes, the previous methods will not work.

## Slide 23: For non-convex polytopes, the previous method requires modification.
Namely, for non-convex polytopes, vertex intersections may include non-adjacent sides
Calculates the vectors pointing inward, vectors normal, vector projections from each vertex per unit cut, and maximum cut distances for each edge
Using the angles and vectors, calculates where the vectors intersect
Finds the minimum distance of intersection
Merges vertices that come together
Repeats

## Slide 24: Step 1: Remains largely the same, to calculate key vectors and angles.
These include:
Unit normal for segment ahead of each vertex
Unit vectors inward at each vertex
Magnitude and direction vector defining vertex motion for a unit cut
Inside the function, the following are also calculated
Distances from vertex-to-vertex,
Unit vectors from vertex to vertex,
[unit_normal_vectors, vertex_projection_vectors] =... fcn_VSkel_fcn_polytopeFindUnitDirectionVectors(vertices,fig_num);

## Slide 25: The magnitude of vertex motion for a unit cut can be found via the following
Given:
Unit normal for segment ahead of each vertex
Unit vectors inward at each vertex
For a unit travel in direction n_i:
And projection vector for unit cut is given by:
[unit_normal_vectors, unit_vertex_projection_vectors, vector_direction_of_unit_cut] = ...
fcn_VSkel_fcn_polytopeFindUnitDirectionVectors(vertices,fig_num);

## Slide 26: Some example results from Step 1

## Slide 27: For each edge, the vertex projections at each end can limit the allowable cut distances
Most vertices will have a finite cut distance. For polytopes that are convex, all vertices have finite cut distances.
fig_num = 0001;
figure(fig_num);
clf;
% this polytope has two nonconvex vertices facing each other
vertices = [5 4; 6 0; 10 0; 10 7; 8 8; 10 9; 10 10; 0 10; 0 0; 4 0; 5 4];
[unit_normal_vectors, unit_vertex_projection_vectors, ~, ~] = ...
fcn_VSkel_polytopeFindUnitDirectionVectors(vertices,-1);
max_edge_cuts = fcn_VSkel_polytopeFindMaxEdgeCut(vertices, unit_normal_vectors, unit_vertex_projection_vectors, (fig_num));

## Slide 28: Step 2: This step uses a function to calculate the smallest radius that is circumscribed at a given vertex
For vertex to edge intersections, given a unit vertex projection, v_i, this vertex will always be on the centerline of any circle center that is tangent to edges to the right and left, e_i and e_i-1. So a projection from another edge must intersect v_j such that the orthogonal distance between both are equal. Note that this method works for any dimension (2D, 3D, and maybe 4+ D)

## Slide 29: This can be solved to determine the projection distance, d, and radius from vertex i to edge j.
The projection distance, d:
The radius:

## Slide 30: Of note, the edge that is tangent may shrink or grow, so we must find tangents not only to the current edge segment, but as well to any extensions

## Slide 31: How does one find which edges participate in the vertex expansion?
The circle center, after it is found, can be projected in the opposite direction of the edge’s unit normal vector, by a radius distance. This projection must either be on the edge for the point to be valid intersection with the segment.
isOnEdge = fcn_INTERNAL_isPointOnEdge(new_edgePointStart,new_edgePointEnd,sphereCenter, flag_do_debug, debug_fig_num);

## Slide 32: Some results from Step 2

## Slide 33: Non-convex case

## Slide 34: Step 3: Find the smallest feasible cut. This is implemented by simply finding the smallest radius among all fitted spheres
Given a unit vertex projection, v_i, this vertex will always be on the centerline of any circle center that is tangent to edges to the right and left, e_i and e_i-1. So a projection from another edge must intersect v_j such that the orthogonal distance between both are equal. Note that this method works for any dimension (2D, 3D, and maybe 4+ D)
fig_num = 1006; figure(fig_num); clf;
% this polytope has a vertical wall
vertices = [0 0; 3/5 0; 1 1; 7/5 0; 2 0; 1 2; 0 1; 0 0]*5;
[unit_normal_vectors, unit_vertex_projection_vectors, vector_direction_of_unit_cut, flag_vertexIsNonConvex] = fcn_VSkel_polytopeFindUnitDirectionVectors(vertices,-1);
max_edge_cuts = fcn_VSkel_polytopeFindMaxEdgeCut(vertices, unit_normal_vectors, unit_vertex_projection_vectors, (-1));
[sphereRadii, definingEdges] = fcn_VSkel_polytopeFindEnclosedSpheres(vertices, unit_normal_vectors, unit_vertex_projection_vectors, vector_direction_of_unit_cut, flag_vertexIsNonConvex, max_edge_cuts, (-1));
[min_cut, ...
indices_repeated, intersection_points] = ...
fcn_VSkel_polytopeFindMinimumEnclosedSphere(vertices, ...
sphereRadii, definingEdges, unit_normal_vectors, unit_vertex_projection_vectors, ...
vector_direction_of_unit_cut, (fig_num));

## Slide 35
https://www.mdpi.com/2220-9964/9/5/304
https://stackoverflow.com/questions/69237154/how-do-you-get-the-medial-axis-of-a-multipolygon-using-cgal
https://groups.csail.mit.edu/graphics/classes/6.838/S98/meetings/m25/m25.html